###### Chapter 04.06

###### Gaussian Elimination – More Examples

###### Chemical Engineering

# Example 1

A liquid-liquid extraction process conducted in the Electrochemical Materials Laboratory involved the extraction of nickel from the aqueous phase into an organic phase. A typical set of experimental data from the laboratory is given below.

| Ni aqueous phase, | 2 | 2.5 | 3 |
| --- | --- | --- | --- |
| Ni organic phase, | 8.57 | 10 | 12 |

Assuming  is the amount of Ni in the organic phase and  is the amount of Ni in the aqueous phase, the quadratic interpolant that estimates  is given by

The solution for the unknowns , , and  is given by

Find the values of , , and  using naïve Gauss elimination. Estimate the amount of nickel in the organic phase when  is in the aqueous phase using quadratic interpolation.

# Solution

# Forward Elimination of Unknowns

Since there are three equations, there will be two steps of forward elimination of unknowns.

## First step

Divide Row 1 by 4 and then multiply it by 6.25, that is, multiply Row 1 by .

Subtract the result from Row 2 to get

Divide Row 1 by 4 and then multiply it by , that is, multiply Row 1 by .

Subtract the result from Row 3 to get

## Second step

We now divide Row 2 by −0.625 and then multiply it by −1.5, that is, multiply Row 2 by .

Subtract the result from Row 3 to get

# Back Substitution

From the third equation,

Substituting the value of  in the second equation,

Substituting the values of  in the first equation,

Hence the solution vector is

The polynomial that passes through the three data points is then

where  is the amount of nickel in the organic phase and  is the amount of nickel in the aqueous phase.

When  is in the aqueous phase, using quadratic interpolation, the estimated amount of nickel in the organic phase is

| SIMULTANEOUS LINEAR EQUATIONS |  |
| --- | --- |
| Topic | Gaussian Elimination – More Examples |
| Summary | Examples of Gaussian elimination |
| Major | Chemical Engineering |
| Authors | Autar Kaw |
| Date | August 8, 2009 |
| Web Site | http://numericalmethods.eng.usf.edu |