###### Chapter 04.08

###### Gauss-Seidel Method – More Examples

###### Chemical Engineering

# Example 1

A liquid-liquid extraction process conducted in the Electrochemical Materials Laboratory involved the extraction of nickel from the aqueous phase into an organic phase. A typical set of experimental data from the laboratory is given below.

| Ni aqueous phase, | 2 | 2.5 | 3 |
| --- | --- | --- | --- |
| Ni organic phase, | 8.57 | 10 | 12 |

Assuming  is the amount of Ni in the organic phase and  is the amount of Ni in the aqueous phase, the quadratic interpolant that estimates  is given by

The solution for the unknowns , , and  is given by

Find the values of , , and  using the Gauss-Seidel method.   Estimate the amount of nickel in the organic phase when 2.3 g/l is in the aqueous phase using quadratic interpolation. Use

as the initial guess and conduct two iterations.

# Solution

Rewriting the equations gives

## Iteration #1

Given the initial guess of the solution vector as

we get

The absolute relative approximate error for each then is

At the end of the first iteration, the estimate of the solution vector is

and the maximum absolute relative approximate error is .

## Iteration #2

The estimate of the solution vector at the end of Iteration #1 is

Now we get

The absolute relative approximate error for each  then is

At the end of the second iteration, the estimate of the solution vector is

and the maximum absolute relative approximate error is .

Conducting more iterations gives the following values for the solution vector and the corresponding absolute relative approximate errors.

| Iteration |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 1 2 3 4 5 6 | 1.3925 2.3053 3.9775 7.0584 12.752 23.291 | 28.1867 39.5960 42.041 43.649 44.649 45.249 | 0.11875 –1.4078 –4.1340 –9.0877 –18.175 –34.930 | 742.1053 108.4353 65.946 54.510 49.999 47.967 | –0.88875 –4.5245 –11.396 –24.262 –48.243 –92.827 | 212.52 80.357 60.296 53.032 49.708 48.030 |

After six iterations, the absolute relative approximate errors are not decreasing much. In fact, conducting more iterations reveals that the absolute relative approximate error converges to a value of  for all three values with the solution vector diverging from the exact solution drastically.

| Iteration |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |

The exact solution vector is

To correct this, the coefficient matrix needs to be more diagonally dominant. To achieve a more diagonally dominant coefficient matrix, rearrange the system of equations by exchanging equations one and three.

## Iteration #1

Given the initial guess of the solution vector as

we get

The absolute relative approximate error for each  then is

At the end of the first iteration, the estimate of the solution vector is

and the maximum absolute relative approximate error is .

## Iteration #2

The estimate of the solution vector at the end of Iteration #1 is

Now we get

The absolute relative approximate error for each  then is

At the end of the second iteration, the estimate of the solution is

and the maximum absolute relative approximate error is .

Conducting more iterations gives the following values for the solution vector and the corresponding absolute relative approximate errors.

| Iteration |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 1 2 3 4 5 6 | 0.88889 0.62309 0.48707 0.42178 0.39494 0.38890 | 12.5 42.659 27.926 15.479 6.7960 1.5521 | 1.3778 1.5387 1.5822 1.5627 1.5096 1.4393 | 27.419 10.456 2.7506 1.2537 3.5131 4.8828 | 2.2589 3.0002 3.4572 3.7576 3.9710 4.1357 | 55.730 24.709 13.220 7.9928 5.3747 3.9826 |

After six iterations, the absolute relative approximate errors seem to be decreasing. Conducting more iterations allows the absolute relative approximate error decrease to an acceptable level.

| Iteration |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 199 200 | 1.1335 1.1337 | 0.014412 0.014056 | –2.2389 –2.2397 | 0.034871 0.034005 | 8.5139 8.5148 | 0.010666 0.010403 |

This is close to the exact solution vector of

The polynomial that passes through the three data points is then

where  is the amount of nickel in the organic phase and  is the amount of nickel in the aqueous phase.

When  is in the aqueous phase, using quadratic interpolation, the estimated amount of nickel in the organic phase is

| SIMULTANEOUS LINEAR EQUATIONS |  |
| --- | --- |
| Topic | Gauss-Seidel Method – More Examples |
| Summary | Examples of the Gauss-Seidel method |
| Major | Chemical Engineering |
| Authors | Autar Kaw |
| Date | August 8, 2009 |
| Web Site | http://numericalmethods.eng.usf.edu |