###### Chapter 03.05

###### Secant Method of Solving a Nonlinear Equation – More Examples

###### Electrical Engineering

# Example 1

Thermistors are temperature-measuring devices based on the principle that the thermistor material exhibits a change in electrical resistance with a change in temperature.  By measuring the resistance of the thermistor material, one can then determine the temperature.

For a 10K3A Betatherm thermistor,

Figure 1 A typical thermistor.

the relationship between the resistance  of the thermistor and the temperature is given by

where  is in Kelvin and  is in ohms.

A thermistor error of no more than  is acceptable. To find the range of the resistance that is within this acceptable limit at , we need to solve

and

Use the secant method of finding roots of equations to find the resistance  at .  Conduct three iterations to estimate the root of the above equation. Find the absolute relative approximate error at the end of each iteration and the number of significant digits at least correct at the end of each iteration.

# Solution

Solving

We get

Let us take the initial guesses of the root of  as and .

## Iteration 1

The estimate of the root is

= 13014

The absolute relative approximate error  at the end of Iteration 1 is

The number of significant digits at least correct is 0, as you need an absolute relative approximate error of less than  for one significant digit to be correct in your result.

## Iteration 2

The estimate of the root is

The absolute relative approximate error  at the end of Iteration 2 is

The number of significant digits at least correct is 1, because the absolute relative approximate error is less than .

## Iteration 3

The estimate of the root is

The absolute relative approximate error  at the end of Iteration 3 is

The number of significant digits at least correct is 3, because the absolute relative approximate error is less than .

| NONLINEAR EQUATIONS |  |
| --- | --- |
| Topic | Secant Method-More Examples |
| Summary | Examples of Secant Method |
| Major | Electrical Engineering |
| Authors | Autar Kaw |
| Date | August 7, 2009 |
| Web Site | http://numericalmethods.eng.usf.edu |

# Text boxes

Tin plated copper alloy lead wires

Thermally conductive epoxy coating