###### Chapter 05.04

###### Lagrange Method of Interpolation – More Examples

###### Electrical Engineering

# Example 1

Thermistors are used to measure the temperature of bodies. Thermistors are based on materials’ change in resistance with temperature. To measure temperature, manufacturers provide you with a temperature vs. resistance calibration curve. If you measure resistance, you can find the temperature. A manufacturer of thermistors makes several observations with a thermistor, which are given in Table 1.

Table 1  Temperature as a function of resistance.

| 1101.0 911.3 636.0 451.1 | 25.113 30.131 40.120 50.128 |
| --- | --- |

Figure 1 Resistance vs. temperature.

Determine the temperature corresponding to 754.8 ohms using a first order Lagrange polynomial.

# Solution

For first order Lagrange polynomial interpolation (also called linear interpolation), the temperature is given by

Figure 2 Linear interpolation.

Since we want to find the temperature at , we need to choose the two data points that are closest to  that also bracket  to evaluate it. The two points are  and .

Then

gives

Hence

You can see that  and  are like weightages given to the temperatures at  and  to calculate the temperature at .

# Example 2

Thermistors are used to measure the temperature of bodies. Thermistors are based on materials’ change in resistance with temperature. To measure temperature, manufacturers provide you with a temperature vs. resistance calibration curve. If you measure resistance, you can find the temperature. A manufacturer of thermistors makes several observations with a thermistor, which are given in Table 2.

Table 2  Temperature as a function of resistance.

| 1101.0 911.3 636.0 451.1 | 25.113 30.131 40.120 50.128 |
| --- | --- |

Determine the temperature corresponding to 754.8 ohms using a second order Lagrange polynomial. Find the absolute relative approximate error for the second order polynomial approximation.

# Solution

For second order Lagrange polynomial interpolation (also called quadratic interpolation), the temperature is given by

Figure 3 Quadratic interpolation.

Since we want to find the temperature at  we need to choose the three data points that are closest to  that also bracket  to evaluate it. The three points are   and .

Then

gives

Hence

The absolute relative approximate error  obtained between the results from the first and second order polynomial is

# Example 3

Thermistors are used to measure the temperature of bodies. Thermistors are based on materials’ change in resistance with temperature. To measure temperature, manufacturers provide you with a temperature vs. resistance calibration curve. If you measure resistance, you can find the temperature. A manufacturer of thermistors makes several observations with a thermistor, which are given in Table 3.

Table 3  Temperature as a function of resistance.

| 1101.0 911.3 636.0 451.1 | 25.113 30.131 40.120 50.128 |
| --- | --- |

- Determine the temperature corresponding to 754.8 ohms using a third order Lagrange polynomial. Find the absolute relative approximate error for the third order polynomial approximation.

- The actual calibration curve used by industry is given by

substituting  and  the calibration curve is given by

Table 4  Manipulation for the given data.

| 1101.0 911.3 636.0 451.1 | 25.113 30.131 40.120 50.128 | 7.0040 6.8149 6.4552 6.1117 | 0.039820 0.033188 0.024925 0.019949 |
| --- | --- | --- | --- |

Find the calibration curve and find the temperature corresponding to 754.8 ohms.  What is the difference between the results from part (a)? Is the difference larger using the results from part (a) or part (b), if the actual measured value at 754.8 ohms is ?

# Solution

a) For third order Lagrange polynomial interpolation (also called cubic interpolation), we choose the temperature given by

Since we want to find the temperature at  we need to choose the four data points that are closest to  that also bracket  to evaluate it. The four data points are    and .

Then

gives

Hence

The absolute relative approximate error  obtained between the results from the second and third order polynomial is

b)  Finding the cubic interpolant using the Lagrangian method of interpolation for

requires that we first calculate the new values of  and .

| 7.0040 6.8149 6.4552 6.1117 | 0.039820 0.033188 0.024925 0.019949 |
| --- | --- |

Then

gives

Hence

Since we’re looking for the temperature at , we will be using

At

Finally, since

Since the actual measured value at 754.8 ohms is  the absolute relative true error between the value used for part (a) is

and for part (b) is

Therefore, a cubic polynomial interpolant given by the Lagrangian method of interpolation, that is,

obtained more accurate results than the calibration curve of

# Text boxes

y

x

(x1, y1)

(x0, y0)

y

x

f1(x)

(x1, y1)

(x0, y0)

f2(x)

(x2, y2)