###### 07.02

###### Trapezoidal Rule for Integration-More Examples

###### Electrical Engineering

# Example 1

All electrical components, especially off-the-shelf components do not match their nominal value.  Variations in materials and manufacturing as well as operating conditions can affect their value. Suppose a circuit is designed such that it requires a specific component value, how confident can we be that the variation in the component value will result in acceptable circuit behavior? To solve this problem a probability density function is needed to be integrated to determine the confidence interval.  For an oscillator to have its frequency within 5% of the target of 1 kHz, the likelihood of this happening can then be determined by finding the total area under the normal distribution for the range in question:

- Use single segment Trapezoidal rule to find the frequency.

- Find the true error, , for part (a).

- Find the absolute relative true error for part (a).

Solution

a)	, where

b) The exact value of the above integral cannot be found. For calculating the true error and relative true error, we assume the value obtained by adaptive numerical integration using Maple as the exact value.

so the true error is

c) The absolute relative true error, , would then be

# Example 2

All electrical components, especially off-the-shelf components do not match their nominal value.  Variations in materials and manufacturing as well as operating conditions can affect their value. Suppose a circuit is designed such that it requires a specific component value, how confident can we be that the variation in the component value will result in acceptable circuit behavior? To solve this problem a probability density function is needed to be integrated to determine the confidence interval.  For an oscillator to have its frequency within 5% of the target of 1 kHz, the likelihood of this happening can then be determined by finding the total area under the normal distribution for the range in question:

- Use 2-segment Trapezoidal rule to find the frequency.

- Find the true error, , for part (a).

- Find the absolute relative true error for part (a).

# Solution

a)

Since,

b) The exact value of the above integral cannot be found.  We assume the value obtained by adaptive numerical integration using Maple as the exact value for calculating the true error and relative true error.

so the true error is

c) The absolute relative true error, , would then be

Table 1 Values obtained using multiple-segment Trapezoidal rule for

Value 1 0.11489 0.86746 88.304 --- 2 0.99638 0.014025 1.4276 88.469 3 0.96093 0.021427 2.1812 3.6891 4 0.96969 0.012670 1.2897 0.90338 5 0.97402 0.0083332 0.84829 0.44455 6 0.97649 0.0058680 0.59734 0.25359 7 0.97801 0.0043459 0.44239 0.15542 8 0.97901 0.0033441 0.34042 0.10214