###### Chapter 03.03

###### Bisection Method of Solving a Nonlinear Equation– More Examples

###### Industrial Engineering

# Example 1

You are working for a start-up computer assembly company and have been asked to determine the minimum number of computers that the shop will have to sell to make a profit.

The equation that gives the minimum number of computers  to be sold after considering the total costs and the total sales is

Use the bisection method of finding roots of equations to find the minimum number of computers that need to be sold to make a profit. Conduct three iterations to estimate the root of the above equation. Find the absolute relative approximate error at the end of each iteration and the number of significant digits at least correct at the end of each iteration.

# Solution

Let us assume

Check if the function changes sign between  and .

Hence

So there is at least one root between  and , that is, between 50 and 100.

## Iteration 1

The estimate of the root is

Hence the root is bracketed between  and , that is, between 50 and 75.  So, the lower and upper limits of the new bracket are

At this point, the absolute relative approximate error  cannot be calculated, as we do not have a previous approximation.

## Iteration 2

The estimate of the root is

Hence, the root is bracketed between  and , that is, between 62.5 and 75.  So the lower and upper limits of the new bracket are

The absolute relative approximate error, at the end of Iteration 2 is

None of the significant digits are at least correct in the estimated root

as the absolute relative approximate error is greater that 5%.

## Iteration 3

The estimate of the root is

Hence, the root is bracketed between  and , that is, between 62.5 and 68.75.  So the lower and upper limits of the new bracket are

The absolute relative approximate error  at the end of Iteration 3 is

Still none of the significant digits are at least correct in the estimated root of the equation, as the absolute relative approximate error is greater than 5%. The estimated minimum number of computers that need to be sold to break even at the end of the third iteration is 69. Seven more iterations were conducted and these iterations are shown in the Table 1.

Table 1 Root of as a function of the number of iterations for bisection method.

Iteration 1 2 3 4 5 6 7 8 9 10 50 50 62.5 62.5 62.5 62.5 62.5 62.5 62.5 62.598 100 75 75 68.75 65.625 64.063 63.281 62.891 62.695 62.695 75 62.5 68.75 65.625 64.063 63.281 62.891 62.695 62.598 62.646 ---------- 20 9.0909 4.7619 2.4390 1.2346 0.62112 0.31153 0.15601 0.077942 76.735 −544.68 −235.12 −79.483 −1.4459 37.627 18.086

At the end of the  iteration,

Hence the number of significant digits at least correct is given by the largest value of  for which

So

The number of significant digits at least correct in the estimated root 62.646 is 2.

| NONLINEAR EQUATIONS |  |
| --- | --- |
| Topic | Bisection Method-More Examples |
| Summary | Examples of Bisection Method |
| Major | Industrial Engineering |
| Authors | Autar Kaw |
| Date | August 7, 2009 |
| Web Site | http://numericalmethods.eng.usf.edu |