###### Chapter 06.03

###### Linear Regression-More Examples

###### Industrial Engineering

# Example 1

As machines are used over long periods of time, the output product can get off target. Below is the average value of how much off target a product is getting manufactured as a function of machine use.

Table 1 Off target value as a function of machine use.

Hours of Machine Use, 30 33 34 35 39 44 45 Millimeters Off Target, 1.10 1.21 1.25 1.23 1.30 1.40 1.42

Regress the data to. Find when the product will be 2 mm off target.

# Solution

Table 2 shows the summations needed for the calculation of the constants of the regression model.

Table 2 Tabulation of data for calculation of needed summations.

I − Hours Millimeters Millimeter-Hour 1 30 1.10 900 33 2 33 1.21 1089 39.93 3 34 1.25 1156 42.50 4 35 1.23 1225 43.05 5 39 1.30 1521 50.70 6 44 1.40 1936 61.6 7 45 1.42 2025 63.9 260 8.91 9852 334.68

mm-h

mm

h

mm-h

Figure 1 Linear regression of hours of use vs. millimeters off target.

Solving for, the regression model is

hours