Multiple-Choice Test

Gauss-Seidel Method of Solving

Simultaneous Linear Equations

1. A square matrix [A]nxn is diagonally dominant if

(A)   i = 1, 2, …, n

(B)   i  = 1, 2, …, n  and  for any i  = 1, 2, …, n

(C)     i = 1, 2, …, n  and  for any i = 1, 2, …, n

(D)    i = 1, 2, …, n

2.  Using [x1   x2   x3] = [1   3   5] as the initial guess, the value of [x1   x2   x3] after three iterations in Gauss-Seidel method for

is

(A)     [-2.8333    -1.4333     -1.9727]

(B)     [1.4959     -0.90464    -0.84914]

(C)     [0.90666   -1.0115      -1.0242]

(D)     [1.2148     -0.72060    -0.82451]

3.  To ensure that the following system of equations,

converges using Gauss-Seidel Method, one can rewrite the above equations as follows:

(A)

(B)

(C)

(D)     The equations cannot be rewritten in a form to ensure convergence.

4.    For and using  as the initial guess, the values of   are found at the end of each iteration as

| Iteration # | x1 | x2 | x3 |
| --- | --- | --- | --- |
| 1 | 0.41666 | 1.1166 | 0.96818 |
| 2 | 0.93989 | 1.0183 | 1.0007 |
| 3 | 0.98908 | 1.0020 | 0.99930 |
| 4 | 0.99898 | 1.0003 | 1.0000 |

At what first iteration number would you trust at least 1 significant digit in your solution?

- 1

- 2

- 3

- 4

5. The algorithm for the Gauss-Seidel Method to solve [A] [X] = [C] is given as follows for using nmax iterations. The initial value of [X] is stored in [X].

- Sub Seidel(n, a, x, rhs, nmax)

For k = 1 To nmax

For i = 1 To n

For j = 1 To n

If (i <> j) Then

Sum = Sum + a(i, j) * x(j)

endif

# Next j

x(i) = (rhs(i) - Sum) / a(i, i)

Next i

Next k

End Sub

(B)       Sub Seidel(n, a, x, rhs, nmax)

For k = 1 To nmax

For i = 1 To n

Sum = 0

For j = 1 To n

If (i <> j) Then

Sum = Sum + a(i, j) * x(j)

endif

# Next j

x(i) = (rhs(i) - Sum) / a(i, i)

Next i

Next k

End Sub

(C)       Sub Seidel(n, a, x, rhs, nmax)

For k = 1 To nmax

For i = 1 To n

Sum = 0

For j = 1 To n

Sum = Sum + a(i, j) * x(j)

# Next j

x(i) = (rhs(i) - Sum) / a(i, i)

Next i

Next k

End Sub

(D)      Sub Seidel(n, a, x, rhs, nmax)

For k = 1 To nmax

For i = 1 To n

Sum = 0

For j = 1 To n

If (i <> j) Then

Sum = Sum + a(i, j) * x(j)

endif

# Next j

x(i) = rhs(i)  / a(i, i)

Next i

Next k

End Sub

6.  Thermistors measure temperature, have a nonlinear output and are valued for a limited range.  So when a thermistor is manufactured, the manufacturer supplies a resistance vs. temperature curve.  An accurate representation of the curve is generally given by

where T is temperature in Kelvin, R is resistance in ohms, and  are constants of the calibration curve.

Given the following for a thermistor

| R | T |
| --- | --- |
| ohm |  |
| 1101.0 911.3 636.0 451.1 | 25.113 30.131 40.120 50.128 |

the value of temperature in for a measured resistance of 900 ohms most nearly is

- 30.002

- 30.472

- 31.272

- 31.445