###### Multiple-Choice Test

###### Chapter 07.05

###### Gauss Quadrature Rule

- is exactly

- For a definite integral of any third order polynomial, the two-point Gauss quadrature rule will give the same results as the

- 1-segment trapezoidal rule

2-segment trapezoidal rule

3-segment trapezoidal rule

Simpson’s 1/3 rule

- The value of  by using the two-point Gauss quadrature rule is most nearly

- 11.672

11.807

12.811

14.633

- A scientist uses the one-point Gauss quadrature rule based on getting exact results of integration for functions  and .  The one-point Gauss quadrature rule approximation for  is

- A scientist develops an approximate formula for integration as

where

The values of  and  are found by assuming that the formula is exact for functions of the form .  The resulting formula would therefore be exact for integrating

- You are asked to estimate the water flow rate in a pipe of radius  at a remote area location with a harsh environment.  You already know that velocity varies along the radial location, but you do not know how it varies.  The flow rate  is given by

To save money, you are allowed to put only two velocity probes (these probes send 	the data to the central office in New York, NY via satellite) in the pipe.  Radial 	location,  is measured from the center of the pipe, that is  is the center of the 	pipe and  is the pipe radius.  The radial locations you would suggest for the 	two velocity probes for the most accurate calculation of the flow rate are

- 0, 2

1, 2

0, 1

0.42, 1.58

For a complete solution, refer to the links at the end of the book.