###### Chapter 10.00F

###### Physical Problem for Partial Differential Equations

###### Industrial Engineering

# Problem Statement

In many inspection processes using vision systems, a camera is used to capture the image of a manufactured part transported on a conveyor. The captured image is processed using an Image Processor to determine the quality of the manufactured part. After the image is processed and the quality of the part is determined as acceptable or defective, an automated sorter is used to separate the defective parts from acceptable ones. Such an application is illustrated in the schematic in Figure 1.

Figure 1:  Vision inspection system schematic

In such systems, it is crucial to set the feed rate of the feeder as high as possible but low enough to avoid any parts passing the end of the conveyor belt without being categorized as acceptable or defective. This is the same as keeping the position of processed parts, denoted by , within the limits of the conveyor belt prior to the parts entering the sorter.

# System Model

In the above described vision inspection system, the number of parts placed on the conveyor by the feeder is equal to the number of parts processed by the sorter. In other words, no parts are removed from the line in the inspection process. Based on this notion, the inspection system can be characterized by a first order partial differential equation as

(1)

with boundary condition and initial condition

where

is the concentration of parts on the transport belt (parts/feet)

is the conveyor speed

is time

is the spatial coordinate variable

is the feed rate of the feeder system (parts/second)

is the initial covering of the conveyor belt

The goal of the system controller is to set the feed rate of the feeder denoted by  such that  (the position where on the conveyor where the part is determined as defective or acceptable) is before the end of the conveyor belt. The velocity  of the decision position is determined by

(2)

Where  is the processing speed of the image reader. When this capacity is divided by the concentration of parts at location , and subtracted from the conveyor speed, the velocity of the decision point is determined.

# Controller Design

The controller for such a system can be designed using several approaches, one of which is based on using optimal-time control as described in [1]. A brief summary of this work is as follows.  For this system to operate within desirable conditions without failing to detect defective parts, the feed rate of the feeder  must be equal to the processing rate  on average. Let loading of the line  describe the number of parts not categorized by the reader. This quantity is determined by the simple differential equation

To hold constant, a switching controller such as

where  is a step function, is used. The feeder works at full capacity  as long as the load of the delay line is less than the reference signal . When it exceeds the reference signal the feeder is stopped. In this manner, the feeder loads the line as quickly as possible when  and the system is emptied as quickly as possible when .

# Questions

1.  Assume that such an inspection system has feed rate of 0.1 parts per second. The imaging process can identify defective/acceptable parts at a rate of 0.12 parts per second. The conveyor speed is set at 2 ft. per second and has a length of 30ft. Calculate the concentration of parts at the midpoint of the conveyor. Assume that there are no parts on the belt at the beginning of the process.

# References

1.   B. Lohman, “Throughput Control for a transport process, and an application in postal automation process”, Control Eng. Practice, 4(11), 1996, p. 1503-1509

| PARTIAL DIFFERENTIAL EQUATIONS |  |
| --- | --- |
| Topic | Physical problem for partial differential equations for chemical engineering |
| Summary | A physical problem of a vision-based inspection system |
| Major | Industrial Engineering |
| Authors | Ali Yalcin |
| Date | June 21, 2011 |
| Web Site | http://numericalmethods.eng.usf.edu |

# Text boxes

vc

p(t)

Image Processor

Sorter

Feeder