###### Chapter 03.03

###### Bisection Method of Solving a Nonlinear Equation – More Examples

###### Chemical Engineering

# Example 1

You have a spherical storage tank containing oil. The tank has a diameter of 6 ft. You are asked to calculate the height  to which a dipstick 8 ft long would be wet with oil when immersed in the tank when it contains 4  of oil.

Figure 1 Spherical storage tank problem.

The equation that gives the height, , of the liquid in the spherical tank for the given volume and radius is given by

Use the bisection method of finding roots of equations to find the height, , to which the dipstick is wet with oil.  Conduct three iterations to estimate the root of the above equation.

Find the absolute relative approximate error at the end of each iteration and the number of significant digits at least correct at the end of each iteration.

# Solution

From the physics of the problem, the dipstick would be wet between  and , where

radius of the tank,

that is

Let us assume

Check if the function changes sign between  and .

Hence

So there is at least one root between  and  that is between 0 and 6.

## Iteration 1

The estimate of the root is

Hence the root is bracketed between  and , that is, between 0 and 3. So, the lower and upper limits of the new bracket are

At this point, the absolute relative approximate error  cannot be calculated, as we do not have a previous approximation.

## Iteration 2

The estimate of the root is

Hence, the root is bracketed between  and , that is, between 0 and 1.5.  So the lower and upper limits of the new bracket are

The absolute relative approximate error  at the end of Iteration 2 is

None of the significant digits are at least correct in the estimated root

as the absolute relative approximate error is greater that .

## Iteration 3

The estimate of the root is

Hence, the root is bracketed between and , that is, between 0 and 0.75.  So the lower and upper limits of the new bracket are

The absolute relative approximate error  at the end of Iteration 3 is

Still none of the significant digits are at least correct in the estimated root of the equation as the absolute relative approximate error is greater than .

The height of the liquid is estimated as 0.75 ft at the end of the third iteration.

Seven more iterations were conducted and these iterations are shown in Table 1.

Table 1 Root of as a function of the number of iterations for bisection method.

Iteration 1 2 3 4 5 6 7 8 9 10 0.00 0.00 0.00 0.00 0.375 0.5625 0.65625 0.65625 0.65625 0.66797 6 3 1.5 0.75 0.75 0.75 0.75 0.70313 0.67969 0.67969 3 1.5 0.75 0.375 0.5625 0.65625 0.70313 0.67969 0.66797 0.67383 ---------- 100 100 100 33.333 14.286 6.6667 3.4483 1.7544 0.86957 −50.180 −13.055 −0.82093 2.6068 1.1500 0.22635 −0.28215 −0.024077 0.10210 0.039249

At the end of the  iteration,

Hence the number of significant digits at least correct is given by the largest value of  for which

So

The number of significant digits at least correct in the estimated root 0.67383 is 2.

| NONLINEAR EQUATIONS |  |
| --- | --- |
| Topic | Bisection Method-More Examples |
| Summary | Examples of Bisection Method |
| Major | Chemical Engineering |
| Authors | Autar Kaw |
| Date | August 7, 2009 |
| Web Site | http://numericalmethods.eng.usf.edu |