###### Chapter 05.03

###### Newton’s Divided Difference Interpolation –

###### More Examples

###### Chemical Engineering

# Example 1

To find how much heat is required to bring a kettle of water to its boiling point, you are asked to calculate the specific heat of water at . The specific heat of water is given as a  function of time in Table 1.

Table 1  Specific heat of water as a function of temperature.

| Temperature, | Specific heat, |
| --- | --- |
| 22 42 52 82 100 | 4181 4179 4186 4199 4217 |

Figure 1 Specific heat of water vs. temperature.

Determine the value of the specific heat at  using Newton’s divided difference method of interpolation and a first order polynomial.

# Solution

For linear interpolation, the specific heat is given by

Since we want to find the velocity at , and we are using a first order polynomial we need to choose the two data points that are closest to  that also bracket  to evaluate it. The two points are  and .

Then

gives

Hence

At ,

If we expand

we get

and this is the same expression as obtained in the direct method.

# Example 2

To find how much heat is required to bring a kettle of water to its boiling point, you are asked to calculate the specific heat of water at . The specific heat of water is given as a function of time in Table 2.

Table 2  Specific heat of water as a function of temperature.

| Temperature, | Specific heat, |
| --- | --- |
| 22 42 52 82 100 | 4181 4179 4186 4199 4217 |

Determine the value of the specific heat at  using Newton’s divided difference method of interpolation and a second order polynomial. Find the absolute relative approximate error for the second order polynomial approximation.

# Solution

For quadric interpolation, the specific heat is given by

Since we want to find the specific heat at , and we are using a second order polynomial, we need to choose the three data points that are closest to  that also bracket  to evaluate it. The three points are   and .

Then

gives

Hence

At

The absolute relative approximate error  obtained between the results from the first and second order polynomial is

If we expand

we get

This is the same expression obtained by the direct method.

# Example 3

To find how much heat is required to bring a kettle of water to its boiling point, you are asked to calculate the specific heat of water at . The specific heat of water is given as a function of time in Table 3.

Table 3  Specific heat of water as a function of temperature.

| Temperature, | Specific heat, |
| --- | --- |
| 22 42 52 82 100 | 4181 4179 4186 4199 4217 |

Determine the value of the specific heat at  using Newton’s divided difference method of interpolation and a third order polynomial. Find the absolute relative approximate error for the third order polynomial approximation.

# Solution

For a third order polynomial, the specific heat profile is given by

Since we want to find the specific heat at , and we are using a third order polynomial, we need to choose the four data points that are closest to  that also bracket . The four data points are    and .

(Choosing the four points as , ,  and  is equally valid.)

then

Hence

At

The absolute relative approximate error  obtained between the results from the second and third order polynomial is

If we expand

we get

This is the same expression as obtained in the direct method.

| INTERPOLATION |  |
| --- | --- |
| Topic | Newton’s Divided Difference Interpolation |
| Summary | Examples of Newton’s divided difference interpolation. |
| Major | Chemical Engineering |
| Authors | Autar Kaw |
| Date | August 12, 2009 |
| Web Site | http://numericalmethods.eng.usf.edu |