###### Chapter 03.04

###### Newton-Raphson Method of Solving a Nonlinear Equation – More Examples

###### Civil Engineering

# Example 1

You are making a bookshelf to carry books that range from 8½" to 11" in height and would take up 29"of space along the length. The material is wood having a Young’s Modulus of , thickness of 3/8" and a width of 12". You want to find the maximum vertical deflection of the bookshelf. The vertical deflection of the shelf is given by

where  is the position along the length of the beam. Hence to find the maximum deflection we need to find where  and conduct the second derivative test.

Figure 1 A loaded bookshelf.

The equation that gives the position  where the deflection is maximum is given by

Use the Newton-Rapshon method of finding roots of equations to find the position  where the deflection is maximum. Conduct three iterations to estimate the root of the above equation. Find the absolute relative approximate error at the end of each iteration, and the number of significant digits at least correct at the end of each iteration.

# Solution

Let us take the initial guess of the root of  as

## Iteration 1

The estimate of the root is

The absolute relative approximate error  at the end of Iteration 1 is

The number of significant digits at least correct is 0, as you need an absolute relative approximate error of less than  for one significant digit to be correct in your result.

## Iteration 2

The estimate of the root is

The absolute relative approximate error  at the end of Iteration 2 is

The number of significant digits at least correct is 1, because the absolute relative approximate error is less than .

## Iteration 3

The estimate of the root is

The absolute relative approximate error  at the end of Iteration 3 is

Hence the number of significant digits at least correct is given by the largest value of  for which

So

The number of significant digits at least correct in the estimated root 14.572 is 6.

| NONLINEAR EQUATIONS |  |
| --- | --- |
| Topic | Newton-Raphson Method-More Examples |
| Summary | Examples of Newton-Raphson Method |
| Major | Civil Engineering |
| Authors | Autar Kaw |
| Date | August 7, 2009 |
| Web Site | http://numericalmethods.eng.usf.edu |