###### Chapter 08.03

###### Runge-Kutta 2nd Order Method for Ordinary Differential Equations-More Examples

###### Computer Engineering

# Example 1

A rectifier-based power supply requires a capacitor to temporarily store power when the rectified waveform from the AC source drops below the target voltage.  To properly size this capacitor a first-order ordinary differential equation must be solved.  For a particular power supply, with a capacitor of , the ordinary differential equation to be solved is

Using the Runge-Kutta 2nd order method, find the voltage across the capacitor at .  Use step size .

# Solution

Per Heun’s method

For

is the approximate voltage at

For

is the approximate voltage at

The results from Heun’s method are compared with exact result of  in Figure 1.

Figure 1 Heun’s method results for different step sizes.

Using smaller step size would increases the accuracy of the result as given in Table 1 and Figure 2 below.

Table 1 Effect of step size for Heun’s method.

Step size, 0.00004 0.00002 0.00001 0.000005 0.0000025 53.307 26.640 15.980 15.918 15.970 37.333 10.666 0.0056605 0.055825 0.0044682 233.71 65.771 0.035436 0.34947 0.027974

Figure 2 Effect of step size in Heun’s method.

In Table 2, the Euler’s method and Runge-Kutta 2nd order method results are shown as a function of step size.

Table 2  Comparison of Euler and the Runge-Kutta methods.

| Step size, |  |
| --- | --- |
|  | Euler | Heun | Midpoint | Ralston |
| 0.00004 0.00002 0.00001 0.000005 0.0000025 | 106.64 53.307 26.640 15.996 15.993 | 53.307 26.640 15.980 15.918 15.970 | 0.026667 0.026667 11.642 15.917 15.968 | 35.529 17.751 15.363 15.917 15.968 |

While in Figure 3, the comparison is shown over the range of time.

Figure 3 Comparison of Euler and Runge-Kutta methods with exact results over time.