###### Chapter 03.03

###### Bisection Method of Solving a Nonlinear Equation – More Examples

###### Electrical Engineering

# Example 1

Thermistors are temperature-measuring devices based on the principle that the thermistor material exhibits a change in electrical resistance with a change in temperature.  By measuring the resistance of the thermistor material, one can then determine the temperature.

For a 10K3A Betatherm thermistor,

Figure 1 A typical thermistor.

the relationship between the resistance  of the thermistor and the temperature is given by

where  is in Kelvin and  is in ohms.

A thermistor error of no more than  is acceptable. To find the range of the resistance that is within this acceptable limit at , we need to solve

and

Use the bisection method of finding roots of equations to find the resistance  at .  Conduct three iterations to estimate the root of the above equation. Find the absolute relative approximate error at the end of each iteration and the number of significant digits at least correct at the end of each iteration.

# Solution

Solving

we get

Lets us assume

Check if the function changes sign between  and .

Hence

So there is at least one root between  and , that is, between  and .

## Iteration 1

The estimate of the root is

Hence the root is bracketed between  and , that is, between  and . So, the lower and upper limits of the new bracket are

At this point, the absolute relative approximate error  cannot be calculated as we do not have a previous approximation.

## Iteration 2

The estimate of the root is

Hence, the root is bracketed between  and , that is, between  and .

So the lower and upper limits of the new bracket are

The absolute relative approximate error  at the end of Iteration 2 is

None of the significant digits are at least correct in the estimated root

as the absolute relative approximate error is greater than .

## Iteration 3

Hence, the root is bracketed between and , that is, between  and .

So, the lower and upper limits of the new bracket are

The absolute relative approximate error  at the end of Iteration 3 is

One of the significant digits is at least correct in the estimated root of the equation as the absolute relative approximate error is less than .

Seven more iterations were conducted and these iterations are shown in the Table 1.

Table 1 Root of as a function of the number of iterations for bisection method. Iteration 1 2 3 4 5 6 7 8 9 10 11000 12500 12500 12875 13063 13063 13063 13063 13074 13074 14000 14000 13250 13250 13250 13156 13109 13086 13086 13080 12500 13250 12875 13063 13156 13109 13086 13074 13080 13077 ---------- 5.6604 2.9126 1.4354 0.71259 0.35757 0.17910 0.089633 0.044796 0.022403

At the end of the iteration,

Hence the number of significant digits at least correct is given by the largest value of  for which

So

The number of significant digits at least correct in the estimated root 13077 is 3.

| NONLINEAR EQUATIONS |  |
| --- | --- |
| Topic | Bisection Method-More Examples |
| Summary | Examples of Bisection Method |
| Major | Electrical Engineering |
| Authors | Autar Kaw |
| Date | August 7, 2009 |
| Web Site | http://numericalmethods.eng.usf.edu |

# Text boxes

Tin plated copper alloy lead wires

Thermally conductive epoxy coating