###### Chapter 07.06

###### Gauss Quadrature Rule for Integration-More Examples

###### Electrical Engineering

# Example 1:

All electrical components, especially off-the-shelf components do not match their nominal value.  Variations in materials and manufacturing as well as operating conditions can affect their value. Suppose a circuit is designed such that it requires a specific component value, how confident can we be that the variation in the component value will result in acceptable circuit behavior? To solve this problem a probability density function is needed to be integrated to determine the confidence interval.  For an oscillator to have its frequency within 5% of the target of 1 kHz, the likelihood of this happening can then be determined by finding the total area under the normal distribution for the range in question:

- Use two-point Gauss quadrature rule to find the frequency.

- Find the absolute relative true error.

# Solution

a) First, change the limits of integration from  to  using

gives

Next, get weighting factors and function argument values for the two point rule,

Now we can use the Gauss Quadrature formula

since

b) The absolute relative true error, , is (Exact value = 0.98236)

# Example 2

All electrical components, especially off-the-shelf components do not match their nominal value.  Variations in materials and manufacturing as well as operating conditions can affect their value. Suppose a circuit is designed such that it requires a specific component value, how confident can we be that the variation in the component value will result in acceptable circuit behavior? To solve this problem a probability density function is needed to be integrated to determine the confidence interval.  For an oscillator to have its frequency within 5% of the target of 1 kHz, the likelihood of this happening can then be determined by finding the total area under the normal distribution for the range in question:

- Use three-point Gauss quadrature rule to find the frequency.

- Find the absolute relative true error.

# Solution:

a) First, change the limits of integration from  to  using

gives

The weighting factors and function argument values are

and the formula is

since

b) The absolute relative true error, , is (Exact value = 0.98236)