###### Chapter 05.04

###### Lagrange Method of Interpolation – More Examples

###### Industrial Engineering

# Example 1

The geometry of a cam is given in Figure 1. A curve needs to be fit through the seven points given in Table 1 to fabricate the cam.

Figure 1 Schematic of cam profile.

Table 1 Geometry of the cam.

Point 1 2.20 0.00 2 1.28 0.88 3 0.66 1.14 4 0.00 1.20 5 –0.60 1.04 6 –1.04 0.60 7 –1.20 0.00

If the cam follows a straight line profile from  to , what is the value of  at  using a first order Lagrange polynomial?

# Solution

For first order Lagrange polynomial interpolation (also called linear interpolation), the value of  is given by

Figure 2 Linear interpolation.

Since we want to find the value of  at , using the two points  and , then

gives

Hence

You can see that  and  are like weightages given to the values of  at  and  to calculate the value of  at .

# Example 2

The geometry of a cam is given in Figure 3. A curve needs to be fit through the seven points given in Table 2 to fabricate the cam.

Figure 3 Schematic of cam profile.

Table 2 Geometry of the cam.

Point 1 2.20 0.00 2 1.28 0.88 3 0.66 1.14 4 0.00 1.20 5 –0.60 1.04 6 –1.04 0.60 7 –1.20 0.00

If the cam follows a quadratic profile from  to  to , what is the value of  at  using a second order Lagrange polynomial? Find the absolute relative approximate error for the second order polynomial approximation.

# Solution

For second order Lagrange polynomial interpolation (also called quadratic interpolation), the value of  given by

Figure 4 Quadratic interpolation.

Since we want to find the value of  at , using the three points , , , then

gives

Hence

The absolute relative approximate error  obtained between the results from the first and second order polynomial is

# Example 3

The geometry of a cam is given in Figure 5. A curve needs to be fit through the seven points given in Table 3 to fabricate the cam.

Figure 5 Schematic of cam profile.

Table 3 Geometry of the cam.

Point 1 2.20 0.00 2 1.28 0.88 3 0.66 1.14 4 0.00 1.20 5 –0.60 1.04 6 –1.04 0.60 7 –1.20 0.00

Find the cam profile using all seven points in Table 3 and a sixth order Lagrange polynomial.

# Solution

For the sixth order polynomial, we choose the value of  given by

Figure 6 6th order polynomial interpolation.

Using the seven points,

gives

Figure 7 Plot of the cam profile as defined by a 6th order interpolating polynomial (using Lagrangian method of interpolation).

# Text boxes

4

y

x

7

6

5

3

4

y

x

7

y

x

f1(x)

(x1, y1)

(x0, y0)

6

5

3

2

1

4

y

x

7

6

5

3

2

1

2

1

(x0, y0)

(x1, y1)

(x2, y2)

f2(x)

x

y

y

x

(x0, y0)

(x1, y1)

(x2, y2)

(x3, y3)

(x4, y4)

(x5, y5)

(x6, y6)

f6(x)