###### Chapter 08.03

###### Runge-Kutta 2nd Order Method for Ordinary Differential Equations-More Examples

###### Industrial Engineering

# Example 1

The open loop response, that is, the speed of the motor to a voltage input of 20V, assuming a system without damping is

If the initial speed is zero; use the Runge-Kutta 2nd order method and a step size of to find the speed at .

# Solution

Per Heun’s method

For

is the approximate speed of the motor at

For

is the approximate speed of the motor at

The exact solution of the ordinary differential equation is given by

The solution to this nonlinear equation at is

The results from Heun’s method are compared with exact results in Figure 1.

Figure 1 Heun’s method results for different step sizes.

Using smaller step size would increases the accuracy of the result as given in Table 1 and Figure 2 below.

Table 1  Effect of step size for Heun’s method.

| Step size, h |  |  |  |
| --- | --- | --- | --- |
| 0.8 0.4 0.2 0.1 0.05 | 160.00 243.20 295.61 301.70 302.79 | 463.09 59.894 7.4823 1.3929 0.30613 | 152.79 19.761 2.4687 0.45954 0.10100 |

Figure 2 Effect of step size in Heun’s method.

In Table 2, the Euler’s method and Runge-Kutta 2nd order method results are shown as a function of step size.

Table 2  Comparison of Euler and the Runge-Kutta methods.

| Step size, h |  |
| --- | --- |
|  | Euler | Heun | Midpoint | Ralston |
| 0.8 0.4 0.2 0.1 0.05 | 800 320 324.8 314.11 308.58 | 160.00 243.20 295.61 301.70 302.79 | 160.00 243.20 295.61 301.70 302.79 | 160.00 243.20 295.61 301.70 302.79 |

In Figure 3, the comparison is shown over the range of time.

Figure 3 Comparison of Euler and Runge-Kutta methods with exact results over time                     (h=0.4).