###### Chapter 05.03

###### Newton’s Divided Difference Interpolation –

###### More Examples

###### Mechanical Engineering

# Example 1

For the purpose of shrinking a trunnion into a hub, the reduction of diameter  of a trunnion shaft by cooling it through a temperature change of  is given by

where

original diameter

coefficient of thermal expansion at average temperature

The trunnion is cooled from  to , giving the average temperature as .  The table of the coefficient of thermal expansion vs. temperature data is given in Table 1.

Table 1  Thermal expansion coefficient as a function of temperature.

| Temperature, | Thermal Expansion Coefficient, |
| --- | --- |
| 80 | 6.47 |
| 0 | 6.00 |
| –60 | 5.58 |
| –160 | 4.72 |
| –260 | 3.58 |
| –340 | 2.45 |

Figure 1 Thermal expansion coefficient vs. temperature.

Determine the value of the coefficient of thermal expansion at  using Newton’s divided difference method of interpolation and a first order polynomial.

# Solution

For linear interpolation, the coefficient of thermal expansion is given by

Since we want to find the coefficient of thermal expansion at  and we are using a first order polynomial, we need to choose the two data points that are closest to  that also bracket  to evaluate it. The two points are  and .

Then

gives

Hence

At

If we expand

we get

This is the same expression that was obtained with the direct method.

# Example 2

For the purpose of shrinking a trunnion into a hub, the reduction of diameter  of a trunnion shaft by cooling it through a temperature change of  is given by

where

original diameter

coefficient of thermal expansion at average temperature

The trunnion is cooled from  to , giving the average temperature as .  The table of the coefficient of thermal expansion vs. temperature data is given in Table 2.

Table 2  Thermal expansion coefficient as a function of temperature.

| Temperature, | Thermal Expansion Coefficient, |
| --- | --- |
| 80 | 6.47 |
| 0 | 6.00 |
| –60 | 5.58 |
| –160 | 4.72 |
| –260 | 3.58 |
| –340 | 2.45 |

Determine the value of the coefficient of thermal expansion at  using Newton’s divided difference method of interpolation and a second order polynomial.  Find the absolute relative approximate error for the second order polynomial approximation.

# Solution

For quadratic interpolation, the coefficient of thermal expansion is given by

Since we want to find the coefficient of thermal expansion at  we need to choose the three data points that are closest to  that also bracket  to evaluate it. The three points are   and .

Then

gives

Hence

At

The absolute relative approximate error  obtained between the results from the first and second order polynomial is

If we expand

we get

This is the same expression that was obtained with the direct method.

# Example 3

For the purpose of shrinking a trunnion into a hub, the reduction of diameter  of a trunnion shaft by cooling it through a temperature change of  is given by

where

original diameter

coefficient of thermal expansion at average temperature

The trunnion is cooled from  to , giving the average temperature as .  The table of the coefficient of thermal expansion vs. temperature data is given in Table 3.

Table 3  Thermal expansion coefficient as a function of temperature.

| Temperature, | Thermal Expansion Coefficient, |
| --- | --- |
| 80 | 6.47 |
| 0 | 6.00 |
| –60 | 5.58 |
| –160 | 4.72 |
| –260 | 3.58 |
| –340 | 2.45 |

- Determine the value of the coefficient of thermal expansion at  using Newton’s divided difference method of interpolation and a third order polynomial.  Find the absolute relative approximate error for the third order polynomial approximation.

- The actual reduction in diameter is given by

where

room temperature

temperature of cooling medium

Since

Find out the percentage difference in the reduction in the diameter by the above integral formula and the result using the thermal expansion coefficient from part (a).

# Solution

a) For cubic interpolation, the coefficient of thermal expansion is given by

Since we want to find the coefficient of thermal expansion at and we are using a third order polynomial, we need to choose the four data points that are closest to  and bracket . These four data points are    and

Then

gives

Hence

At

The absolute relative approximate error  obtained between the results from the second and third order polynomial is

b) In finding the percentage difference in the reduction in diameter, we can rearrange the integral formula to

and since we know from part (a) that

Combining like terms, we get

We see that we can use the integral formula in the range from  to

Therefore,

So  using the actual reduction in diameter integral formula. If we use the average value for the coefficient of thermal expansion from part (a), we get

and  using the average value of the coefficient of thermal expansion using a third order polynomial. Considering the integral to be the more accurate calculation, the percentage difference would be

| INTERPOLATION |  |
| --- | --- |
| Topic | Newton’s Divided Difference Interpolation |
| Summary | Examples of Newton’s divided difference interpolation. |
| Major | Mechanical Engineering |
| Authors | Autar Kaw |
| Date | August 12, 2009 |
| Web Site | http://numericalmethods.eng.usf.edu |