###### Chapter 07.02

###### Trapezoidal Rule for Integration-More Examples

###### Mechanical Engineering

# Example 1

A trunnion of diameter  has to be cooled from a room temperature of  before it is shrink fit into a steel hub (Figure 1).

Figure 1 Trunnion to be slid through the hub after contracting.

The equation that gives the diametric contraction, in inches of the trunnion in dry-ice/alcohol (boiling temperature is ) is given by:

- Use single segment Trapezoidal rule to find the contraction.

- Find the true error, , for part (a).

- Find the absolute relative true error for part (a).

# Solution

a)	, where

b) The exact value of the above integral is

so the true error is

c) The absolute relative true error, , would then be

# Example 2

A trunnion of diameter  has to be cooled from a room temperature of  before it is shrink fit into a steel hub (Figure 1).  The equation that gives the diametric contraction, in inches of the trunnion in dry-ice/alcohol (boiling temperature is ) is given by:

Use two segment Trapezoidal rule to find the contraction.

- Find the true error, , for part (a).

- Find the absolute relative true error for part (a).

# Solution

a) The solution using 2-segment Trapezoidal rule is

b) The exact value of the above integral is

so the true error is

c) The absolute relative true error, , would then be

Table 1 Values obtained using multiple-segment Trapezoidal rule for

Value 1 0.013521 0.00016810 1.2280 --- 2 0.013647 0.30700 0.92328 3 0.013670 0.13644 0.16825 4 0.013679 0.076750 0.059740 5 0.013682 0.049120 0.027644 6 0.013684 0.034111 0.015014 7 0.013686 0.025061 0.0090522 8 0.013687 0.019188 0.0058749